## Slide 1
Giuseppe Frau (Deep Blue)
01 July 2022
Human Factor Assessment

## Slide 2
Human Performance Validation Objectives
Impact of contingency situation on safety
Roles, responsibilities, operating methods and human tasks
Technical support systems and Human-Machine Interface
Team structure and Communication
Remote Pilot and Controller Acceptability
Remote Pilot and Controller Competence

## Slide 3
Human Performance Assessment - RTS Challenges
2 Parallel RTSs
Same RWC instrument but different setups / environment
Different teams observing the RTS
Different cultures/experience of the involved RPAS pilots
Potentially high number of variables
Target airspace classes (D to G)
RPAS performance, Traffic Load, Traffic Type, Timing, Airspace Transitions,
Controlled Variables
Need to introduce “noise”/non-nominal situations to test the instrument

## Slide 4
Human Performance Assessment Preliminary Results
Improved Situation Awareness
Improvement of SA also in cases of non-cooperative (no transponder) vehicles detected through RWC sensors. Class E especially.
Improvement on the projection dimension of SA, i.e. knowing in advance the escape direction
HMI was suitable for the instrument and task
type of alerts well distinguished and manoeuvres suggestion easy to interpret
timing of the alerts fine tuned after RTS1 and RTS2
Integration with the rest of the RPAS control instruments to be carefully considered
Position of the RWC screen related to other instruments, for example close to autopilot. “Especially in case of latency I need to keep an eye on the RWC while I provide the commands for the maneuver”
Avoid overlap of functions/visualization
Highly dependent on the specific pilot position

## Slide 5
Roles and Responsibilities
Responsibilities of Remote Pilot and ATC must be clear in all the Airspace Classes according to the ATC service level provided.
RWC should not be used to self-separation in controlled airspaces
Timing
When in controlled airspaces with high occupancy of radio frequency, time needed for interactions with ATC increases and available maneuvering time might become too tight.
Latency of the RPAS controls is an additional important factor to be considered
Human Performance Assessment Preliminary Results

## Slide 6
Procedures
Procedures should be defined in order to avoid too many calls from RPAS to ATC: e.g. only call when RWC alerts pilot, not when traffic is only displayed, do not request for separation too soon
Transparency & Training
Better transparency on the coverage of the sensors: variable from vehicle to vehicle and there should be a way to know it from the HMI + specific training must be provided
Non cooperative traffic not shown on ATC CWPs creates information asymmetry that can only be be leveled through communication between pilot and ATC therefore augmenting communication load and frequency occupation
Human Performance Assessment Preliminary Results

## Slide 7
THANK YOU FOR
YOUR ATTENTION